## Slide 1
Contents
1. Introduction & Project Overview
2. System Architecture Design
3. Transmitter Hardware Components
4. Receiver Hardware Components
5. Circuit Integration & Wiring
6. Wireless Protocol: ESP-NOW
7. Mecanum Wheel Kinematics
8. Software Control Firmware
9. Calibration & Physical Assembly
10. Performance Testing & Future Scope

## Slide 2
1. Introduction & Project Overview
• Natural Human-Machine Interfaces (HMI): Traditional joysticks and remote controllers require physical contact and manual dexterity. This project provides an intuitive alternative.
• Gesture-Based Motion Control: Translates natural wrist tilt gestures (Pitch and Roll orientation angles) directly into mobile chassis steering vectors.
• ESP32 Microcontrollers: High-performance microcontrollers establish a direct peer-to-peer 2.4 GHz connection without a wireless router.
• Core System Applications: Ideal for heavy warehouse logistics, search-and-rescue operations in hazardous environments, and assisting individuals with limited mobility.

## Slide 3
2. System Architecture Design
• Transmitter Wearable Glove:
Interfaces the MPU6050 6-axis motion sensor with the transmitter ESP32 to compute static tilt angles.
• Direct Wireless Link:
Transmits orientation packages wirelessly via connectionless ESP-NOW protocol at 2.4 GHz.
• Receiver Mobile Chassis:
Decodes the incoming commands and regulates motor speed and direction using dual L298N motor drivers.

## Slide 4
3. Transmitter Hardware Components
• ESP32 Dev Board (Transmitter):
32-bit dual-core processor running at 240 MHz. Reads sensor data and packages wireless commands.
• MPU6050 6-Axis Motion Sensor:
Combines a 3-axis accelerometer and a 3-axis gyroscope on a single silicon die. Measures gravitational tilt.
• I2C Serial Interface:
Communicates over the I2C bus: SDA connected to GPIO 21, SCL connected to GPIO 22.

## Slide 5
4. Receiver Hardware Components
• ESP32 Dev Board (Receiver):
Receives ESP-NOW packet payloads, triggers callback routines, and generates PWM/digital logic.
• Dual L298N H-Bridge Drivers:
Provides current amplification (up to 2A per channel) and independent speed/direction control to all 4 motors.
• Actuators & Power Pack:
Four 200 RPM dual shaft BO geared motors powered by a high-capacity 7.4V series 18650 Li-Ion battery pack.

## Slide 6
5. Circuit Integration & Wiring
• Direct Pin Assignments:
Maintains independent inputs: ENA, IN1-IN4, and ENB for both Front and Back driver boards.
• PWM Speed Control:
ESP32 outputs analog-mapped PWM values (0-255) to the ENA/ENB enable pins to regulate motor speed.
• Common Ground System:
Requires tying the GND pins of the ESP32, battery pack, and driver boards together to establish a stable reference voltage.

## Slide 7
6. Wireless Protocol: ESP-NOW
• Connectionless Communication: Operates directly on the 2.4 GHz band. Bypasses the pairing, handshaking, and router routing overhead of standard Wi-Fi.
• Ultra-Low Latency: Minimizes command propagation delays to under 10 milliseconds, enabling instantaneous chassis response to hand gestures.
• Media Access Control (MAC) Address Pairing: Secure peer-to-peer unicast connection requires uploading a helper sketch to read the receiver's physical 48-bit MAC address.
• Transmission Range: Achieves a stable, noise-immune operational range of up to 45 meters under active line-of-sight test environments.

## Slide 8
7. Mecanum Wheel Kinematics
• Holonomic Steering Mechanics:
Rollers mounted at 45-degree angles create directional force vectors that combine to allow lateral sliding, diagonal drive, and spot rotation.
• Movement Matrix Logic:
Controlling individual wheel rotation directions enables 360-degree holonomic mobility without changing vehicle orientation.
Robot Action | FL Wheel | FR Wheel | BL Wheel | BR Wheel
Forward | Forward | Forward | Forward | Forward
Backward | Reverse | Reverse | Reverse | Reverse
Lateral Left | Reverse | Forward | Forward | Reverse
Lateral Right | Forward | Reverse | Reverse | Forward
Stop | Stop | Stop | Stop | Stop

## Slide 9
8. Software Control Firmware
• Orientation Calculations: Transmitter reads raw accelerometer data from the MPU6050 over the hardware I2C bus and calculates hand Pitch and Roll angles using trigonometric functions.
• Noise Filtering: Compliments raw values using complementary filters to eliminate high-frequency engine and chassis vibrations.
• Mapping & Struct Packaging: Maps calculated tilt angles to a standard 0-254 range. Structures and broadcasts data packets to the receiver MAC.
• Decisive Steering: Receiver callback function executes instantly. Reads structural data and steers the wheels based on threshold parameters (Neutral, Forward, Reverse, Left Slide, Right Slide, and Diagonal drift).

## Slide 10
9. Calibration & Physical Assembly
• Threshold Calibration:
Neutral flat state mapped around values 310-350. Tilted states calibrated around thresholds (< 290 and > 370).
• Wearable Gesture Glove Setup:
MPU6050 and ESP32 transmitter secured to a wearable glove to match natural hand movements.
• Assembled 4WD Vehicle:
Geared BO motors, L298N drivers, battery pack, and ESP32 receiver consolidated onto a stable 4WD mobile platform.

## Slide 11
10. Performance Testing & Evaluation
• Signal Latency:
Achieves a highly responsive latency of 8 ms.
• Wireless Range:
Maintains stable wireless communication up to 45 meters.
• Operating Time:
2200 mAh Li-Ion battery pack delivers 45 minutes of continuous operational runtime.

## Slide 12
11. Conclusions & Future Scope
• Key System Realization: Successfully developed a low-latency connectionless ESP-NOW mobile robotic vehicle driven by wearable MPU6050 accelerometer wrist tilt gestures.
• Functional Execution: Physical calibration and testing confirmed instant steering response (Neutral, Forward, Reverse, Lateral Left/Right, Diagonal Drift) with high noise immunity.
• Core Future Directions:
- Replace L298N drivers with high-efficiency TB6612FNG drivers to optimize current draw.
- Integrate ultrasonic and LiDAR sensors to implement autonomous obstacle avoidance.
- Implement sensor fusion and Kalman filtering for precise gyroscope angle tracking.
- Integrate with the Robot Operating System (ROS) for autonomous warehouse fleet routing.